## Slide 1: Automation Communication Protocols
Alyssa Dedolph
Advanced Applications Group

## Slide 2: TwinCAT Connectivity Big Picture
194/212/229
PC Hardware
TwinCAT 3
153/42/108
Connectivity
153/42/108
PLC
153/42/108
PLC
Safety
153/42/108
Motion
153/42/108
CCAT
Modules
153/42/108
Simulink®
Module
153/42/108
Measurement
and Analytics
153/42/108
Vision Runtime
153/42/108
HMI
153/42/108
CNC
153/42/108
Robotics Motion
153/42/108
IoT Communication
HTTPs
MQTT
153/42/108
Database Connection
153/42/108
TCP/IP
153/42/108
153/42/108
ADS
153/42/108
EtherCAT Automation Protocol
153/42/108
PROFINET, EtherNet/IP,
Modbus
153/42/108
M2M
153/42/108
MES / WES
153/42/108
HMI
153/42/108
MATLAB®
153/42/108
LabView®
Cloud Connectivity + Analytics
DB
ERP
RS232
RS485

## Slide 3: TwinCAT IoT product overview
Easy integration of IoT communication protocols
Multiple protocols available: MQTT, HTTPS, OPC UA Pub/Sub, WebSockets, OCPP
Smartphone App available for Android and iOS
TF6701 IoT Communication
MQTT client connectivity
Real-time driver for the PLC
TF6720 IoT Data Agent
IoT gateway application
Standalone tool
TF6710 IoT Functions
Data Agent access
Real-time driver for the PLC
TF6760 IoT HTTP/REST
HTTP(S) client connectivity
Real-time driver for the PLC
TF6770 IoT WebSockets
WebSockets client/server
Real-time driver for the PLC
TF6730 IoT Communicator
Smartphone App
TF6020 JSON Data Interface
Req/Res MQTT connectivity
ADS interface for PLC
TF6105 OPC UA Pub/Sub
OPC UA Pub/Sub connectivity
MQTT, UDP
MQTT, WSS,
HTTPS, OCPP,
OPC UA
Microsoft Azure
Thingspeak
TF6771 IoT OCPP
OCPP client connectivity
OCPP server connectivity
Real-time driver for the PLC
TwinCAT Cloud Engineering
MQTT, WSS,
HTTPS, OCPP,
OPC UA
MQTT, WSS,
HTTPS, OCPP,
OPC UA

## Slide 4: TwinCAT Connectivity MQTT
“A lightweight, publish-subscribe, machine to machine network protocol.”
Originally designed for remote sites with low-bandwidth or unreliable networks.
Why is MQTT ideal for IoT?
  Simple
    Pub/sub simplifies device communications and routing
    Supports multiple data formats
  Secure
    Supports TLS (certificate-based encryption)
  Performant

## Slide 5: TwinCAT Connectivity Traditional MES Communication Model
IT System
Networking
IP Address: 10.10.1.10
Protocol: ModbusTCP
Data Address: 432770
Data Format: 2x 16-bit words
Transaction
OT System
IP Address: 10.10.2.10
Protocol: Beckhoff ADS
Data Address: ‘PLC1.MAIN.eStatus’
Data Format: 1x 32-bit DINT
Transaction
To transact with each OT device, we need:
  Networking
    Security, firewall
    Address routing, NAT
  Application protocol driver
    Port numbers
    Device/node addressing
    Vendor software
  Data address and type information
    Type systems
    Byte packing, endianness
OT System
OT System
IP Address: …
Protocol: …
Data Address: …
Data Format: …
Transaction
Address Table
---------------
Machine1: 10.10.1.10
Machine2: 10.10.2.10
Machine#: 10.10.x.x
…

## Slide 6: TwinCAT Connectivity Broker Pub/Sub Model
IT System
To transact with each OT device, we need:
  Broker address
  Topic
Payloads can be binary or JSON (human-readable)
New components can simply connect to the broker and can begin publishing/subscribing
Topics created as needed, with user-defined names and “paths”:
Broker
OT System
Broker: 10.10.0.1
Topic: Machine/1/Status
Data: { ‘status’: ‘running’ }
Publish
OT System
Broker: 10.10.0.1
Topic: Machine/2/Status
Data: { ‘status’: ‘idle’ }
Publish
OT System
Subscribe
---------------
Broker: 10.10.0.1
Topic: Machine/#
Broker: 10.10.0.1
Topic: Machine/3/Status
Data: { ‘status’: ‘running’ }
Publish
Topic Subscription Messages Received
------------------- ---------------------------------
Machine/# All messages from all machines
Machine/1/# All messages from machine 1
Machine/1/Status Machine 1 status messages
Machine/+/Status Status messages from all machines

## Slide 7: TwinCAT Connectivity QoS and Retain
QoS (Quality of Service) – Means of guaranteeing message transfer to the broker, specified by the client
  Level 0: At most once
  Level 1: At least once
  Level 2: Exactly once
Retain – Mechanism for ensuring a subscriber received the message.
  A flag to inform the broker to hold onto the most recent “retain” message for a topic
  Any client subscribing to the topic, before or after the publish, will receive this message
Notes: QoS level 0
At this QoS level the receiver does not acknowledge receipt. The message is not sent a second time.
QoS level 1
At this QoS level the system guarantees that the message arrives at the receiver at least once, although the message may arrive more than once. The sender stores the message internally until it has received an acknowledgment from the receiver in the form of a PUBACK message. If the PUBACK message fails to arrive within a certain time, the message is resent.
QoS level 2
At this QoS level the system guarantees that the message arrives at the receiver no more than once. On the MQTT side this is realized through a handshake mechanism. QoS level 2 is the most secure level (from a message transfer perspective), but also the slowest. When a receiver receives a message with QoS level 2, it acknowledges the message with a PUBREC. The sender of the message remembers it internally until it has received a PUBCOMP. This additional handshake (compared with QoS 1) is important for avoiding duplicate transfer of the message. Once the sender of the message receives a PUBREC, it can discard the initial publish information, since it knows that the message was received once by the receiver. In other words, it remembers the PUBREC internally and sends a PUBREL. Once the receiver has received a PUBREL, it can discard the previously remembered states and respond with a PUBCOMP, and vice versa. Whenever a packet is lost, the respective communication device is responsible for resending the last message after a certain time.

## Slide 8: TwinCAT Connectivity Broker Scalability
Broker
Broker
Broker
Broker
Broker: cloud.broker.com
Topic: Site/1/Machine/2/Status
Data:
{
‘status’: ‘running’,
‘ppm’: 12.32,
‘uptime: ‘3:54:21’
…
}
Subscribe
Site 2
Site 1
Site 3
https://web.portal.com/site/1/machine/2/status
Broker-to-broker communications and cloud hosted brokers facilitate distributed, scalable connectivity
Formalize topic naming and hierarchy (“namespaces”) to organize site, machine and component level data
Web service can be introduced for external access
cloud.broker.com
2
3
1
Web server

## Slide 9: TwinCAT Connectivity Lab 1 – MQTT
Open MQTT Client of choice
Connect to iot.beckhoff.us:1883 (User: BausUser PW: TwinCAT)
  Depending on client, you may need to subscribe to ‘#’ to see all incoming messages (there will be tons)
  Unsubscribe from ‘#’ and subscribe to ‘nem_2026/#’
Reference and follow lab guide: https://github.com/andedolph/NEM_2026_Connectivity

## Slide 10: TwinCAT Connectivity TF6760
TF6760 TC3 IoT HTTPS/REST
  HTTPS client connectivity for TwinCAT 3 PLC
  Allows to send HTTPS requests (GET, POST, PUT, ...)
  Perfectly suited for web services that offer a REST API
  Security via SSL/TLS
Web service with
REST API
TF6760 IoT HTTPS/REST
HTTPS

## Slide 11: TwinCAT Connectivity HTTP/REST
Hyper Text Transfer Protocol (HTTP) is the ubiquitous language for web sites and services
Representational State Transfer (REST) is a set of architectural guidelines for web-based applications
  Describes how web clients and servers should interact at a high level
  “RESTful” APIs commonly use HTTP
Tons of technology relies on HTTP, not just websites:
  Native apps, mobile apps
  Package Managers
  Commercial systems; ERP, CMS, POS, etc.
  SaaS, PaaS systems
Very mature and comprehensive ecosystem of tooling
  Development tools, libraries
  Security, access control, encryption
Notes: Enterprise Resource Planning, content management system, point of sale

## Slide 12: TwinCAT Connectivity HTTP/REST
Hyper Text Transfer Protocol (HTTP) is the ubiquitous language for web sites and services
The most common HTTP methods are GET, POST, and PUT
  GET – Requests a resource from the server
  POST – Transfers data to the server
  PUT – Replaces or creates a resource on the server with the request payload
Notes: The POST method is used to request that the origin server accept the entity enclosed in the request as a new subordinate of the resource identified by the Request-URI in the Request-Line.
The PUT method requests that the enclosed entity be stored under the supplied Request-URI. If the Request-URI refers to an already existing resource, the enclosed entity SHOULD be considered as a modified version of the one residing on the origin server. If the Request-URI does not point to an existing resource, and that URI is capable of being defined as a new resource by the requesting user agent, the origin server can create the resource with that URI.

## Slide 13: TwinCAT Connectivity HTTP/REST Query Parameters
  Query parameters are used to specify resources from a server in a way which sorts/filters the resources.
  https://www.beckhoff-weather.com/forecast?city=verl
  https://www.beckhoff-weather.com - Domain
  /forecast - Path
  ?city=verl - Query parameter, where ‘?’ indicates the start of the query string

## Slide 14: TwinCAT Connectivity TF6760 Application Examples
Telegram: Messaging application with REST API
  „Telegram-Bot“ is used for communication
Philips Hue: Smart home system
  Philips Hue bridge is the central unit
  Bridge offers REST API to control devices
OpenWeatherMap: REST API for weather data
  Different weather data formats
  Location-based requests

## Slide 15: TwinCAT Connectivity HTTP/REST – Exercises
Exercise 1: Web Browser
  Open your browser of choice
  Open developer tools (usually Ctrl + Shift + i)
  Open the ‘Network’ tab
  Load a web page – observe requests
    Markup, binary data (e.g. images), JavaScript, JSON – all retrieved via HTTP requests
Exercise 2: cURL, wget, Invoke-WebRequest
  Open a PowerShell terminal
  Use any one of the above commands
  Type in an endpoint, e.g. ‘httpbin.org/get’
Samples: https://github.com/Beckhoff/TF6760_Samples
  Postman
  OpenWeatherMap

## Slide 16: TF6105 | TC3 OPC UA Pub/Sub
Implements OPC UA Pub/Sub (OPC10000-14)
Supported transport protocols:
  UDP: use case “Device-to-Device”
  MQTT: use case “Device-to-Cloud”
Supported operating system platforms:
  Windows 10/11 (32-bit/64-bit)
  TwinCAT/BSD
  TwinCAT/Linux (32-bit/64-bit)
Message Broker
3rd-Party application
TF6105 OPC UA Pub/Sub
3rd-party application
Pub/Sub MQTT
Pub/Sub MQTT
Pub/Sub UDP

## Slide 17: Client/Server vs. Pub/Sub
OPC UA has had a client/server architecture since its beginning in 2006
This has been perfectly suited for direct communication between devices, e.g. an HMI that directly connects to the PLC to read data
However there are challenges:
  Firewalls that need to be configured in order to allow access
  Poor scalability to hundreds or even thousands of devices
  Poor performance because of the underlying TCP channel that is used for client/server
TF6100 OPC UA Client/Server
3rd Party OPC UA Client/Server
3rd Party OPC UA Client/Server

## Slide 18: Should I use OPC UA Pub/Sub or MQTT?
Inhomogeneous environments with different vendors make interoperability a challenge
Remember: MQTT only standardizes transport, the data format is up to the application
Therefore OPC UA Pub/Sub and MQTT complement each other very well:
  MQTT provides standardized transport
  OPC UA provides standardized data format
{
Timestamp : x,
Values : {
Var1 : 42
}
}
{
DayTime : x,
Var1 : 42.0
}
OPC UA object
(Binary, JSON)
MQTT payload:
3rd Party
MQTT payload:
MQTT payload:
Application
Message Broker

## Slide 19: TwinCAT Cloud Engineering
TwinCAT Cloud Engineering is a cloud service that provides virtual-machines with pre-installed TwinCAT + Functions
Platform-independent, secure access to the virtual machine via regular web browser
Secure access to physical controller via ADS-over-MQTT - perfectly suited for remote maintenance
Connected machine
User
TwinCAT Cloud Engineering
TwinCAT
Analytics
TwinCAT
Engineering
TwinCAT
PLC
TwinCAT
Connectivity
Message Broker
TwinCAT
ML Runtime
TwinCAT
HMI
ADS-over-MQTT
HTTPS